|  | REGISTERED / IMMEDIATE Heavy Industries Taxila Project Directorate ARDIC Taxila Cantonment Tel: 051-9315589 Fax: 051-9315151 No. 5646/IT- 13/Proc/ARDIC 02 Nov 2023 |
| --- | --- |

To:		M/s __________________________

Subject:	Tender Inquiry Proc of Eddy Current Equipment

1.	You are requested to please forward your quotation for the following item. Detail of item required with terms and conditions are given below:-

| Ser | Nomenclature | A/U | Qty | Remarks |
| --- | --- | --- | --- | --- |
| 1. | Eddy Current Test Equipment Country of Origin: UK, USA, Germay, Japan or equivalent Specification: Model: AeroCheck+ or equivalent Gain: Overall: -18 to +100dB,0.1,1and 6dB steps(100dB maximum) Input: 0 dB or 12 dB Drive: 0dB,6dB and 10dB(0dB reference 1mW into 50 ohm) Max X/Y Ratio: +/-100dB Phase: Range: 0°-359.9°,0.1° steps or equivalent Auto phase: Allows phase angle to be automatically set to a preset angle Filters: Normal High pass: DC to 2kHz or low pass filter, whichever is the lower in 1Hz steps, plus variable adaptive balance drift compensation 0.01-0.5 Hz(6 steps). Normal Low Pass: 1 Hz to 2kHz or a quarter of the lowest test frequency, whichever is lower in 1 Hz steps. Balance: Manual:14 internal balance loads,2.2µH,5.0µH,6.0µH,6.5µH,7.0µH,7.5µH ,8.2µH,12µH,15µH,18µH,22µH,30µH,47µH,82µH Automatic: Optimized balance load selection Alarms: Box: Fully configurable Freeze, Tone or visual. Sector: Fully configurable Freeze, Tone or visual. Output: open collector transtor(50v dc at 10mA max) available on 12 way lemo. Display: Type: Min 5.7” (145mm), 18 bit color, daylight readable. Viewable Area: 115.2mm(Horizontal) x 86.4mm(vertical) or better Resolution: 640 x 480 pixels or better Offset: spot position: Y=-50 to +50,X=-65 to +65% or better Removable Data Storage: Setup Storage: microSD upto 32GB min Stored Screen shots: microSD upto 32GB min Record Replay: Real time recording upto 164 Seconds Verification Level: The system include on delivery a 2 years validity verification Level 2 detailed functional check and calibration as per ISO 15548-1:2013 Power: Running Time: Up to 8hrs with a 2MHz pencil probe 30% back light and up to 6hrs with a rotary drive at 3000rpm 50% duty cycle. Surface probe pencil: Surface probe pencil absolute (PS200PS028-114N) 200KHz,28mm tip length Surface probe pencil bridge (PS200PS028-114NB) 200KHz,28mm tip length Surface probe pencil right angle (PS200PR050-114N) 200KHz,5mm tip length Test Block: Test block ATBF, ferrous ( steel EN1A), 0.2,0.5,1.0mm slots Lead Lemo: Lead lemo 12 way to microdot 1.5m absolute Lead lemo 00 to microdot 1.5m Lead lemo 12-way to lemo 4 way 1.5m (reflection) Lead lemo 12 way to lemo 4 way 1.5m (Bridge) Case: Instrument soft carry case Training: Comprehensive 2 x weeks training from level III qualified person will be given by the firm regarding operation, fault location, safety parameters and trouble shooting of system | Nos | 01 |  |

////

(Item One Only)

Instructions to Bidders

2.	All documents required to evaluate technical proposal must be marked against serial no mentioned in IT and Flagged properly for identification. Index sheet to the ocuments attached in proposal be provided.

3.	All financial documents must be audited by authorized third party registered auditor which can be verified at any stage of whole procurement/contracting process.

4.	Any false statement may lead to disqualification of bidder and legal action will be taken as per PPRA rules.

5.	Rates will be quoted on FOR Taxila Cantt basis. Offer best competitive price while submitting your quotation.

6.	Any interlineations, erasures, or overwriting shall be valid only if they are signed by the person or persons signing the Bid.

7.	All Bidders are required to submit the bid offer letter comprising particulars of the firm as per Bid Submission Form att Anx-‘A’, Bidder information Form Anx-‘B’ duly signed and stampe by authorized representative of the firm.

8.	Single Stage Two Envelope Procedure will be followed. Part-I and Part-II quotations will be enclosed in separate sealed envelopes for each tender inquiry. For identification purpose, the words “TECHNICAL QUOTATION PART-I WITHOUT PRICE” and COMMERCIAL QUOTATION (PART-II) WITH PRICE” shall be written in BLOCK CAPITAL LETTERS on the respective sealed envelopes which will be placed in a large envelope bearing complete details of the tender as under: -

Please forward your quotation not later than   05 Dec 2023 at 10:30 hours. The address on the envelope will be indicated as under: -

BID								                           REGISTERED

TENDER INQUIRY NO. 5646/IT-13/Proc/ARDIC dated 02 Nov 2023

TO BE OPENED ON. 05 Dec 2023

To:		PROCUREMENT OFFICER

ARDIC HIT TAXILA CANTT

FROM 	M/S	________________________

IT FOR      	________________________

9.	Delivery of Tender:	The tender/bid will be enclosed in a sealed envelope which will be invariably marked with “Bid against Tender Inquiry No. 5646/IT- 13/Proc/ARDIC dated 02 Nov 2023” and complete address. The tender if brought by hand, will be handed over to security staff on duty at ARDIC Gate for placing the same in bid box (available at the gate). The bid will not be brought by hand by any firm while visiting the office of Proc officer (ARDIC). Moreover if required endorsements are found missing, the bid will be liable for rejection.

10.	The bid must be dropped in the bid box, latest by 1030 hours on  05 Dec 2023, at ARDIC Gate. The bid will be opened same day at 1100 hours in the presence of the available representative of the firms in ARDIC HIT Taxila Cantt. No bid will be entertained / considered after 1030 hours, on the aforementioned date.

11.	All papers must be signed and stamped and items not quoted / quoted must be mentioned clearly.

12.	All clauses/terms mentioned in this inquiry will be considered accepted by the bidding firms, even if no reference to them is given in the respective offers.

13.	Compliance to the Standard Bidding Documents developed by PPRA in pursuance of Sec 27 of PPRA Ordinance,2022 read with rule 23(4) of Public Procurement Rules 2004, S.R.O 370(I)/2022 is mandatory and can be obtained from PPRA website www.ppra.org.pk.

14.	Postal order for Rs. 500/- (Rupees Five Hundred) as a tender fee, in favor of MD (ARDIC) HIT Taxila Cantt, will invariably be enclosed with the technical offer, failing which the bid will be ignored.

15.	Firms are instructed NOT to send Telex and Fax bids. Such bids/offers would not be accepted.

16.	Please confirm receipt of the tender inquiry immediately and also intimate your participation or otherwise in this tender inquiry. In case any firm does not wish to bid, then it should return the tender inquiry documents at the earliest.

17.	HIT reserves its right to cancel the bidding process with reason but without any obligation to justify such a reason.

18.	The store is required to be delivered at Store Sec ARDIC, Taxila Cantt within 03 x Months from the date of signing of the contract.

19.	The offered price quoted must be firm, final and inclusive of all taxes, packing, handling charges etc and delivery at HIT Taxila Cantt.

20.	Offers must remain open valid for 120 days from the date of opening of the tender.

21.	The store will be packed in standard grade, worthy of transportation by the means adopted.

22.	This inquiry may not be taken as an indication of subsequent supply order and does not in any way commit HIT to purchase the items offered.

23.	Warranty period will be one year from the date of issuance of CRV of the stores.

24.	In case of failure to supply the stores within the stipulated periods, liquidated damages (LD) at the rate of 2% but not less than 1% of amount involved per month and maximum value not more than 10% of contracted store value or a part there-of will be levied.

25.	Payment Terms

a.	Payments will be made by CMA (DP), Rawalpindi or CMA (HIT) Taxila Cantt, 		through cheques against pre-	receipted bills (duly affixed with revenue stamps) 			alongwith professional tax certificates (attested photocopies) of the suppliers 			after delivery and acceptance of stores.

b.	Partial payments against partial delivery is not allowed.

c.	The payment to the registered person is linked with active taxpayer status of the 			Suppliers as per FBR data base. If any registered supplier is not on active 			Taxpayer list, his payment will be stopped till he / she files his / her mandatory 			returns and appears on ATL of FBR.

26.	HIT reserves the right to increase / decrease the quantity of items, placed on the tender without any reference to the firm.

27.	5% performance bank guarantee (PBG) provided during the contract signing stage, against the total value of contract. This bank guarantee must remain valid 12 x months after the stores are put in operation. Performance Bank Guarantee will be released on the completion of warranty period, in case the firm fails to provide a/m performance bank guarantee within the stipulated time period, the contract will be cancelled and bid security will be encashed. Moreover, the contract shall than be awarded to next best evaluated bidder.

28.	All Firms participating in the tender will deposit an amount of Rs. 200,000/- as bid security in the shape of CDR / bank guarantee addressing in the name of Managing Director (ARDIC) Heavy Industries Taxila. The bid security will be provided in original by the firms in TECHNICAL QUOTATION and clear mentioning of the same failing which the bid will stand rejected. The bid securities will be returned as under:-

a.	Unsuccessful Bidders.	Within 15 days of completion/ 									announcement of the bid evaluation result.

b.	Successful Bidders.     	Upon submission of 5% PBG.

29.	The net offered price will be inclusive of 18 % GST or as per applicable Govt rules at the time of contract. The offers without mentioning of 18% GST will not be considered. The GST will always be mentioned separately to the base price.

30.	Defaulted or Blacklisted firms with any Govt / Semi Govt defence organization cannot participate in the bid.

31.	In case of any dispute regarding the terms and conditions and the quality of stores, the decision of the MD (ARDIC)/Chairman HIT will be considered as final and binding on the suppliers/firms.

32.	In case, the contracted firm fails to execute the order within the stipulated time and does not materialize the supply of ordered stores, the supply order/contract would be cancelled at the firm's risk and expense. Expenditure incurred on the re-purchase of offered stores will be recovered from the defaulting firm, under existing procedures.

33.	Inspection of the store will be carried out at (ARDIC) HIT Taxila Cantt. The store will be inspected/ tested in presence of firm representative. All store will be physically inspected by inspection board to confirm that item is new & packed as per specification. Item should be fully functional, otherwise it will be rejected.

34.	Only registered suppliers / persons who are on Active Taxpayer List (ATL) of FBR are eligible to supply goods/services to government departments. Thus the bidders will submit a certificate to this regard along with the technical bid.

35.	Country of Origin: All countries except India and Israel are eligible.

36.	In the case of FOR imported items, the firms are responsible to provide evidence of the agency agreement/certificate of conformance, principal proforma invoice (in original and without price) and OEM certificates of all the items being quoted against this tender inquiry along with countries of origin. Separate OEM certificate for each / major assembly will be provided by the firms. The firms will clearly indicate that all the parts used in the manufacturing (in case of assembling) are brand new from current production. Confirmation to fulfill technical specifications related to imported items on FOR basis must be highlighted in the technical bid.

37.	Confirmation of the validity period of the quote, delivery period and warranty period.

38.	Confirmation of all technical parameters specified in the IT or confirmation as per sample.

39.	Confirmation of manufacturer, brand and Approval of Advance Sample (where ever asked) as per specifications mentioned in IT. Manufacturer brand of each item must be highlighted in the bid.

40.	Manual / work instructions and consumable spares may also be provided with the equipment.

41.	All the potential firms are strongly encouraged to apply and give consent of participation in this IT, well before time. Any request for extension in opening date should reach this office at least 48 hours before closing dates and time. Such request should not be considered as binding on HIT for Estension and remains HIT’s preropgative to safeguard and decide whether to extend or not.

42.	Testing Method:   Testing of equipment will be carried out against IT specifications and OEM operating manual procedures.

43.	Eligibility Criteria

  - Firms should not be blacklisted or defaulted anywhere within or outside Pakistan. In this regard firm should provide “No Blacklisting” (affidavit on judicial stamp as per Annexure ‘C’, duly attested by Notary Public, to be provided).

  - Only FBR registered suppliers / persons who are on Active Taxpayer List (ATL) of FBR are eligible to supply goods/services to government departments. Thus the bidders will submit a certificate to this regard along with the technical bid.

  - In case of indigenously / locally manufactured item, the firms should have relevant experience and capacity of manufacturing these parts and should be duly qualified by Quality Control Department of ARDIC Capacity for manufacturing of parts will be verified by a team ex ARDIC during technical scrutiny of offer.

  - In the case  of  FOR  imported  items,  the  firms  are responsible to provide evidence of the agency agreement/certificate of conformance, principal proforma invoice (in original and without price) and OEM certificates of all the items being quoted against this tender inquiry along with countries of origin. The firms will clearly  indicate  that  all  the  parts  used  in  the manufacturing (in case of assembling) are brand new from  current  production. Confirmation to fulfill technical specifications related to imported items on FOR basis must be highlighted in the technical bid.

  - Confirmation of the validity period of the quote, delivery period and warranty period.

  - Confirmation of all technical parameters specified in the IT or confirmation as per sample.

44.	Qualification Criteria. Performance and Technical Evaluation will only be used as qualification criteria with 70% passing marks in Performance Evaluation and 70% passing marks in Technical Evaluation. Out of qualified bidder, best Evaluated bid having least cost only will be considered. “Conformance to IT specifications is mandatory”.

| Cat | Mks | % Weight age |  | Remarks |
| --- | --- | --- | --- | --- |
| Performance Evaluation | 30 | 30 |  | Minimum 70% in each Group 1st Lowest |
| Technical Evaluation | 70 | 70 |  |  |
| Price Evaluation | 100 | 100 |  |  |

  - Marks Distribution Qualification Matrix

| Ser | Description | Maximum Points |
| --- | --- | --- |
| Performance Evaluation |  |
| 1) | Financial Soundness | 15 |
| 2) | Past Experience / Record | 15 |
| Technical Evaluation |  |
| 3) | Project’s Technical Evaluation criteria | 70 |
| Total | 100 |

  - Financial soundness. Credit marks for financial soundness of the firm 	shall be   on the basis of following qualifications:-

| Ser | Description | Max Points | Explanation for Marks Obtained | Remarks |
| --- | --- | --- | --- | --- |
| (a) | Annual turnover of last 3 x Financial Years | 5 | Marks will be calculated as per the formula:- Formula Score = (Y1+Y2+Y3) x5 3X *(Y1,Y2,Y3 respective annual turnovers of last three years) X= Last purchased rate / estimated value of the quoted items available with HIT. | Third Party generated verifiable audit reports for last three financial years to be provided and up to and greater than Rs 5 Mn. Else income tax return for last 3x years fully verified by ITO of the circle. Note All calculation will be done in Rs, other currency (if any) will be converted into Rs. With applicable conversion rate. |
| (b) | Working Capital of last 3 x Financial years | 10 | Marks will be calculated as per the formula:- Formula Score= (Y1+Y2+Y3) x10 3(x/2) Y1, Y2 and Y3 being respective working capitals of last three years. X/2= Half of the last purchased rate OR estimated value of the quoted items available with HIT. |  |
|  | Total | 15 |  |  |

  - Past Experience/ Previous Record. Credit marks for experience  shall  	be awarded on the basis of following qualifications:-

| Ser | Description | Max Points | Explanation for Marks Obtained | Remarks |
| --- | --- | --- | --- | --- |
| (a) | Projects of similar nature and complexity i.e. Procurement of Volumetric Titrator equivalent completed in last 3 years. | 10 | years (1.3 marks per contract Maximum 3.3 marks per year) | Attested and verifiable copies of related contracts / Purchase orders with Government / Semi Government / Defence organization be attached. |
| (b) | Status of enlistment with Government Organizations (Attested copies of Registration certificates to be enclosed). | 5 | Not registered firms will be awarded 2.5 gratis Marks |  |
|  | Total | 15 |  |  |

  - Project’s Technical Evaluation. Credit Marks shall be granted on the basis of the following criteria for evaluation:-

| Ser | Description | Max Points |
| --- | --- | --- |
| a) | Conformance with IT specifications | Mandatory |
| b) | Delivery period will be calculated as under:- 2 x Months = 15 Marks ii. 3 x Months = 10 Marks | 15 |
| c) | Free of cost on job training (user level, Technical, Adv Technical) | 30 |
| d) | Provision of free of cost warranty (1 x Year = 15, 2 x Year = 25) | 25 |
| e) | Total | 70 |

45.	Contracts will be awarded to best evaluated bidder using least cost method.

Note: Technical / Commercial quotation must conform to IT parameters specified in this tender. The offer will be rejected there in if the said parameters are not complied with.

|  | Maj Procurement Officer (Said Saddam Hussain) |
| --- | --- |

Annexure ‘C’

IT No. 5646/IT- 13/2023-24/FOR/ARDIC/Proc

Dated 02 Nov 2023

AFFIDAVIT

# NO BLACK LISTING CERTIFICATE

It is certified that M/s ______________________________________ have never been blacklisted with any Govt / Semi Govt / Defence Organization / PPRA / KPK PPRA / Punjab PPRA / Sindh PPRA within or outside Pakistan.

___________________________ (Designation, Signature & Stamp)

____________________________

(Signature & Stamp of Notary Public)

Annexure-‘A’

BID SUBMISSION FORM

Name of Bidder: [__________________________] Date: __________________

Name of Bidding Firm: [__________________________________________]

BID NUMBER: ____________________________________________________

I the undersigned, offer to supply the ____________and related Services (if required) for the __________________________________________________in accordance with your Invitation to Bid No______________________________.

I hereby submit my bid, which includes Technical Bid and Commercial Bid/Price Schedule.

I certified that I/my CEO, his partners and my firm, named --------------------:

have not been suspended, debarred, sanctioned or otherwise identified as ineligible by any Govt or any other organization

have not been blacklisted from any govt or any other organization

have no conflict of interest in accordance with Instruction to Bidders

I declare that all the information and statements made in this bid are true and I accept that any misinterpretation or misrepresentation contained in this bid may lead to my and my firm disqualification from this tender.

I offer to supply the _________ in conformity with the bidding documents.

My bid shall be valid and remain binding upon me for the period specified in the Bid Data Sheet.

I understand and recognize that you are not bound to accept any bid you receive.

I, the undersigned, certify that I am duly authorized by [_____________________] to sign this bid and bind it should HIT accept the bid

Name:	____________________________

Title: _______________________________

Date: _______________________________

Signature: ____________________________

[Stamp with official stamp of the bidder]

Annexure-‘B’

BIDDER INFORMATION FORM

| Name of the Bidder |  |
| --- | --- |
| Name of the Bidding Firm |  |
| Address |  |
| Tel Number | Line Cell |
| Bidder Registration Status with other Organizations | Permanent Registered with -------- Provisional Registered with ---- Not Registered |
| Status of Firm | Manufacturer/Stockiest/Importer, etc |
| Bidder Authorized Representative | Name: Cell Number: |
| Contact Person for Firm | Name: Cell Number: |
| Number of Employees with Firm |  |
| Any Certification Held with Firm with Validity Period |  |
| Bidder Email Address, if any |  |
| Fax Number, if any |  |
| OEM of Firm by whom store is manufactured |  |
| Principal of Firm from whom store will be provided |  |